## Slide 1: MemBo: Runtime Memory Borrowing on UPMEM-based Servers
Student: 李昀澤
Advisor: Da-Wei Chang, Ph. D.
July 28, 2023
Operating System and Embedded System Lab

## Slide 2: Background-UPMEM Introduction
First real-world Processing in Memory (PIM) hardware (2019)
  Programmable near memory co-processors
  Integrate RISC processors, called Data Processing Units (DPUs), into a DRAM DIMM
UPMEM PIM DIMMs
An UPMEM-based Server
UPMEM, “UPMEM Website,” https://www.upmem.com, 2023.

## Slide 3: Background-UPMEM-based System
UPMEM PIM acceleration model
Typical DRAM module
Typical DRAM module
UPMEM DRAM module
UPMEM DRAM module
Typical DRAM module
UPMEM DRAM module
Host CPU
Conventional
DIMM
UPMEM
PIM DIMM (16 chips)
DPU
Control interface
DDR4 Interface
DRAM
(MRAM)
IRAM
WRAM
PIM Chip
x8
Input data copy
Instruction scratchpad memory
Data scratchpad memory
Allocate DPUs in ranks
(64DPUs per rank).
DPU application
DRAM bank used for CPU-DPU data exchange
Output data copy

## Slide 4: Background-UPMEM-based System
Current OS design: MRAM is statically reserved for DPU applications
Typical DRAM module
Typical DRAM module
UPMEM DRAM module
UPMEM DRAM module
Typical DRAM module
UPMEM DRAM module
Host CPU
Conventional
DIMM
UPMEM
PIM DIMM (16 chips)
DPU
Control interface
DDR4 Interface
DRAM
(MRAM)
IRAM
WRAM
PIM Chip
x8
DPU input/output data copy
Statically reserved for the DPU
Even when the DPU is idle

## Slide 5: Background-Memory Usage Variance
Machines ID
Datacenters at Alibaba and Google reports greatly time-varying memory utilization per machine
C. Lu, K. Ye, G. Xu, C.-Z. Xu, and T. Bai, “Imbalance in the cloud: An analysis on Alibaba cluster trace”, in 2017 IEEE International Conference on Big Data (Big Data), 2017, pp. 2884–2892.
Memory Utilization
Time (hour)

## Slide 6: Background-Computing Resource Usage Variance
In heterogeneous computing environments such as GPU platforms or UPMEM PIM platforms, there is also a dynamic variation in the demand for computing resources
K. Mahajan et al., “Themis: Fair and efficient {GPU} cluster scheduling,” in 17th USENIX Symposium on Networked Systems Design and Implementation (NSDI 20), 2020, pp. 289–304.

## Slide 7: Motivation-Addressing Memory Usage Variance on UPMEM servers
Problem: The current policy of statically reserving MRAM for DPU applications fails to fully utilize MRAM to accommodate the time-varying main memory and DPU usage
Host CPUs
Trigger page swapping
System throughput 
The idle MRAM banks are wasted!
Typical DRAM module
Typical DRAM module
Typical DRAM module
Conventional
DIMM
UPMEM DRAM module
UPMEM DRAM module
UPMEM DRAM module
UPMEM
PIM DIMM
High memory pressure!
System Memory

## Slide 8: Solution-MemBo
Solution: we propose MemBo, a runtime memory borrowing mechanism on UPMEM-based servers
  Enables the memory allocator to borrow idle MRAM as system memory when facing high memory demand
Objectives
  Increase the utilization/flexibility of MRAM resources and minimize the occurrence of costly swapping operations
  An OS level approach: transparent to both UPMEM server administrators and users

## Slide 9: MemBo-High Level Overview
MemBo triggers MRAM borrowing when the system faces high memory pressure
High memory pressure!
Try to borrow idle MRAM
Host CPUs
Typical DRAM module
Typical DRAM module
Typical DRAM module
Conventional
DIMM
UPMEM DRAM module
UPMEM DRAM module
UPMEM
PIM DIMM
System Memory
Alleviate or release!

## Slide 10: MemBo-High Level Overview
Two reclamation scenarios
  When the memory pressure is released (background)
  When a DPU application arrives and requires the borrowed MRAM (foreground)
Reclaim borrowed MRAM
Memory pressure released
Host CPUs
Typical DRAM module
Typical DRAM module
Typical DRAM module
Conventional
DIMM
UPMEM DRAM module
UPMEM DRAM module
UPMEM
PIM DIMM
System Memory

## Slide 11: MemBo-High Level Overview
Activate a DPU process and allocate DPU ranks
No enough ranks left for the DPU user due to MRAM borrowing!
Startup delay 
Two reclamation scenarios
  When the memory pressure is released (background)
  When a DPU application arrives and requires the borrowed MRAM (foreground)
Host CPUs
Typical DRAM module
Typical DRAM module
Typical DRAM module
Conventional
DIMM
UPMEM DRAM module
UPMEM DRAM module
UPMEM
PIM DIMM
System Memory
Live data
Live data
Live data
Challenge:
Minimizing the delay

## Slide 12: Current System Architecture and Design Issues
`
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Buddy System
Non-DPU Applications
UPMEM Driver
UPMEM SDK
MRAM Banks
Zone fallback list
Design Issues
How to enable the MRAM borrowing mechanism?
Who/When to trigger MRAM borrowing/
reclamation?
3. How to minimize the overhead of foreground reclamation?

## Slide 13: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads

## Slide 14: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
High Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Modify the zone fallback list setup for MemBo

## Slide 15: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Extend the UPMEM driver to provide two new MRAM page operations:
MRAM borrowing operation
MRAM reclamation operation
borrowed MRAM pages

## Slide 16: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Introduce new kernel threads to automate the MRAM borrowing/reclamation operations

## Slide 17: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Provides MemBo compatible DPU allocation APIs, which are transparent to DPU programmers.

## Slide 18: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Provides optional foreground reclamation time minimization APIs

## Slide 19: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
High Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Modify the zone fallback list setup for MemBo

## Slide 20: Memory Zone Setup in MemBo
MemBo insert ZONE DEVICE into the fallback list of buddy system during the initialization phase, but hide all the MRAM pages from the buddy system (free page lists are not built)
Fallback order design principles
  MRAM pages should be used only after ZONE_DEVICE’s pages are nearly exhausted -> MRAM pages are more expensive since they need to be reclaimed
  ZONE_DEVICE locates at high-memory address and can be reclaimed at any time -> MRAM pages are not compatible for performing DMA operations
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
ZONE DMA
Memory Zone Fallback List

## Slide 21: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Extend the UPMEM driver to provide two new MRAM page operations:
MRAM borrowing operation
MRAM reclamation operation
borrowed MRAM pages

## Slide 22: MRAM Borrowing/Reclamation Operations
MRAM pages borrowing operation
  Re-initialize the metadata for the MRAM pages (e.g., struct page)
  Insert the MRAM pages into the free lists of ZONE_DEVICE
MRAM pages reclamation operation
  Migrate any live data on the MRAM pages to ZONE_NORMAL and hide the pages from the buddy system
  Re-initialize the metadata for the MRAM pages
Granularity of the operations
  Rank granularity is too high, leading to the following problems
    Holding the locks for a long period, blocking other operations to ZONE_DEVICE
    Borrowing MRAM pages that exceed the demand
  We use 64MB in our current design

## Slide 23: MRAM Borrowing/Reclamation Operations: Borrowed MRAM Page Placement Policy
Problem: DPU allocations and MRAM borrowing are implemented in different granularities
  DPU rank allocation granularity (4GB) vs. MRAM borrowing granularity (64MB)
(b) Need page migration
(a) No need of page migration

## Slide 24: MRAM Borrowing Interface: Borrowed MRAM Page Placement Policy
MemBo maintains two linked lists to manage the borrowed MRAM pages placement
unborrowed rank list
borrowed rank list
…
Used by DPU
Used by buddy system
Free

## Slide 25: MRAM Borrowing Interface: Borrowed MRAM Page Placement Policy
MemBo UPMEM driver maintains two linked lists to manage the borrowed MRAM pages placement
unborrowed rank list
borrowed rank list
…
Used by DPU
Used by buddy system
Free
…
borrow_mram_pages/
reclaim_mram_pages
64MB

## Slide 26: MRAM Borrowing Interface: Borrowed MRAM Page Placement Policy
MemBo UPMEM driver maintains two linked lists to manage the borrowed MRAM pages placement
unborrowed rank list
borrowed rank list
…
Used by DPU
Used by buddy system
Free
…
…
borrow_mram_pages/
reclaim_mram_pages
64MB

## Slide 27: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Introduce new kernel threads to automate the MRAM borrowing/reclamation operations

## Slide 28: Who trigger MRAM Borrowing/Reclamation Operations?
MemBo includes two kernel threads to cooperate with the buddy system to automate the borrowing/reclamation operations
  MemBo manager
    Wake up by the high memory pressure detector in the buddy system (low memory watermark)
    initiate an MRAM borrowing operation
  MemBo reclaimer (background reclamation)
    Periodically check if the memory pressure of ZONE_NORMAL has released (high memory watermark)
    Initiate MRAM reclamation operations

## Slide 29: When to trigger MRAM Borrowing Operations?
Linux buddy system uses the memory watermark WMARK_LOW to control the fallback timing and the activation of swapping operations
WMARK_LOW
(1) Try the next zone in the fallback list
(2) If (1) fails, the free pages # drops below WMAKR_LOW, and the buddy system trigger swapping operations (wakeup kswapd)
Free pages # of ZONE_DEVICE
Time

## Slide 30: When to trigger MRAM Borrowing Operations?
The buddy system makes sure that the free pages number in ZONE_DEVICE stays higher than WMARK_LOW through MemBo manager
Free pages # of ZONE_DEVICE
Time
An allocation fallback to ZONE_DEVICE.
(indicating low free memory in ZONE_NORMAL)
WMARK_LOW
High memory pressure detector wakeup MemBo manager for first borrowing.
High memory pressure detector wakeup MemBo manager for second borrowing.
t

## Slide 31: Who trigger MRAM Borrowing/Reclamation Operations?
MemBo includes two kernel threads to cooperate with the buddy system to automate the borrowing/reclamation operations
  MemBo manager
    Wake up by the high memory pressure detector in the buddy system (low memory watermark)
    initiate an MRAM borrowing operation
  MemBo reclaimer (background reclamation)
    Periodically check if the memory pressure of ZONE_NORMAL has released (high memory watermark)
    Initiate MRAM reclamation operations

## Slide 32: When to trigger Background MRAM Reclamation Operations?
The MemBo reclaimer periodically (0.1s) check if the memory pressure of ZONE_NORMAL has released and trigger MRAM background reclamation
free pages # of ZONE_NORMAL
time
WMARK_LOW
WMARK_HIGH_MEMBO
MemBo reclaimer initiates MRAM borrowing operations, migrating live data back to free ZONE_NORMAL’s pages.
MemBo reclaimer is activated once the first MRAM borrowing completes
512 MB
t

## Slide 33: Architecture of MemBo
ZONE NORMAL
ZONE
DMA32
ZONE DEVICE
(reserved MRAM pages)
ZONE DMA
Conventional
DRAM Banks
Operating System
Kernel Space
Hardware
Operating System User Space
DPU Applications
Non-DPU Applications
MemBo
Library
MRAM Banks
Modified Zone Fallback List
MRAM Borrowing Interface
Modified UPMEM Driver
MemBo Manager
MemBo Reclaimer
Modified UPMEM SDK
Memory Pressure Detector
Modified Buddy System
MemBo Kernel Threads
Provides optional foreground reclamation time minimization APIs

## Slide 34: Recap-Foreground Reclamation Challenge
Activate a DPU process and allocate DPU ranks
No enough ranks left for the DPU user due to MRAM borrowing!
Startup delay 
Foreground reclamation may increase the latency of the DPU application
Host CPUs
Typical DRAM module
Typical DRAM module
Typical DRAM module
Conventional
DIMM
UPMEM DRAM module
UPMEM DRAM module
UPMEM
PIM DIMM
Live data
Live data
Live data

## Slide 35: Solution 1-Data Migration Pipelining (DMP)
Main idea: pipeline the foreground reclamation time and the DPU input data copy time
  rank level data migration parallelism
CPU copies input data to DPUs
DPU execution
CPU retrieves result from DPUs
With foreground reclamation
Data migration pipelining
Without foreground reclamation
Latency
1-rank reclamation
1-rank input data copy
Foreground
reclamation
CPU copies input data to DPUs
DPU execution
CPU retrieves result from DPUs
DPU execution
CPU retrieves result from DPUs

## Slide 36: MemBo Library-DMP Implementation APIs and Coding Example
dpu_alloc_ranks_membo_dmp
  Users can pass a callback function, which is called whenever a part of required ranks is reclaimed
  Input data copy operations for the reclaimed rank can be initiated in the callback function

## Slide 37: Solution 2-DPU Usage Prediction-based Rank Reservation (PBRR)
UPMEM DRAM module
Typical DRAM module
Typical DRAM module
Typical DRAM module
UPMEM DRAM module
Host CPUs
Main Memory
MRAM
DPU usage predictor
Periodically predict the DPU usage in the near future
reserved
Prediction result: 3 ranks required in the near future
Main idea: periodically predict the DPU usage in the near future
  Trigger MRAM background reclamation in advance and prevent foreground reclamation
MemBo borrows the idea from LirCUP, a linear regression based resource usage prediction method
Conventional DRAM DIMMs
UPMEM PIM DIMMs
2 free ranks left
F. Farahnakian, P. Liljeberg, and J. Plosila, “LiRCUP: Linear Regression Based CPU Usage Prediction Algorithm for Live Migration of Virtual Machines in Data Centers”, in 2013 39th Euromicro Conference on Software Engineering and Advanced Applications, 2013, pp. 357–364.

## Slide 38: MemBo Library-PBRR Implementation APIs
MemBo library provides the following DPIs for predictor implementation
  get_dpu_usage
    Get the current DPU usage (in rank)
  set_membo_reservation_threshold
    Set the number of rank reservation

## Slide 39: Evaluation Setup
CPU | Intel Xeon Silver 4208 CPUs @ 2.10GHz
Conventional DIMMs | 64GB DDR4 DRAM
UPMEM PIM DIMMs | 16 dual rank UPMEM PIMM DIMMs Total DPUs: 1024 DPUs @350GHz Total MRAM: 64GB
Operating System | Distro: Ubuntu 20.04 Linux kernel: 5.15.45 (MemBo) UPMEM driver: 2021.3.0 (MemBo)
UPMEM SDK | UPMEM SDK 2021.3.0 (MemBo)
SSD | SAMSUNG 980 PRO NVMe SSD 2TB (used as swap space)

## Slide 40: Workloads
YCSB workloads (left) and DPU applications from PrIM (right)
YCSB workloads are executed on Memcached, a popular key-value store
Workload | Operation | Request Distribution
A | 50% Read, 50% Write | Zipfian
B | 95% Read, 5% Write | Zipfian
C | 100% Read | Zipfian
D | 95% Read, 5% Write | Latest
F | 50% Read, 50% Read-Modify-Write | Zipfian
DPU Application | Input Size
VA | 25M elements/DPU rank
SEL | 
UNI | 
RED | 
SCAN-RSS | 
SCAN-SSA | 
TRNS | 12288 × 16 × 1024 × 8/16 DPU ranks
BS | 25M elements, 25M queries/DPU rank
J. Gómez-Luna, I. El Hajj, I. Fernandez, C. Giannoula, G. F. Oliveira, and O. Mutlu, “Benchmarking Memory-Centric Computing Systems:
Analysis of Real Processing-In-Memory Hardware”, in 2021 12th International Green and Sustainable Computing Conference (IGSC), 2021, pp. 1–7.
B. F. Cooper, A. Silberstein, E. Tam, R. Ramakrishnan, and R. Sears, “Benchmarking Cloud Serving Systems with YCSB”, in Proceedings of the 1st ACM Symposium on Cloud Computing, Indianapolis, Indiana, USA, 2010, pp. 143–154.

## Slide 41: Experimental Groups
To evaluate the scalability of MemBo, we configure the following experimental groups
  Baseline: Native UPMEM platform without MemBo
  MemBo(k): MemBo is enabled, and k ranks are available for MRAM borrowing

## Slide 42: Evaluation Scenarios
One YCSB workload
  Throughput Improvement of YCSB
  Major page faults reduction
One YCSB workload + one DPU application
  DPU application runtime
  Throughput Improvement of YCSB
  Effectiveness of data migration pipelining
One YCSB workload + multiple DPU applications
  Effectiveness of prediction-based rank reservation
  Throughput Improvement of YCSB

## Slide 43: Evaluation Scenarios
One YCSB workload
  Throughput Improvement of YCSB
  Major page faults reduction
One YCSB workload + one DPU application
  DPU application runtime
  Throughput Improvement of YCSB
  Effectiveness of data migration pipelining
One YCSB workload + multiple DPU applications
  Effectiveness of prediction-based rank reservation
  Throughput Improvement of YCSB

## Slide 44: YCSB Performance Improvement: YCSB Workloads 50M items/operations
Throughput improvement (left) and major page faults reduction (right)
Workload D shows a better spatial locality, limiting the benefit of MemBo.
2.42x
1.22x

## Slide 45: YCSB Performance Improvement: YCSB Workloads 100M items/operations
Throughput improvement (left) and major page faults reduction (right)

## Slide 46: Memory Capacity Variation
MemBo can expand/shrink the memory capacity based on the memory pressure
MemBo trigger MRAM borrowing when facing high memory pressure, expand the memory capacity
MemBo reclaimer reclaims the borrowed pages when the memory pressure is released

## Slide 47: Evaluation Scenarios
One YCSB workload
  Throughput Improvement of YCSB
  Major page faults reduction
One YCSB workload + one DPU application
  DPU application runtime
  Throughput Improvement of YCSB
  Effectiveness of data migration pipelining
One YCSB workload + multiple DPU applications
  Effectiveness of prediction-based rank reservation
  Throughput Improvement of YCSB

## Slide 48: Scenario 2-One YCSB workload + one DPU application
Evaluation steps
1. Launch YCSB workload A (100M items and operations)
2. After 5 minutes, activate a 16-rank DPU application, triggering MRAM reclamation
3. Collect the overall throughput of YCSB workload A and the runtime of the DPU application

## Slide 49: YCSB Throughput Variation in Time
Launch YCSB A

## Slide 50: YCSB Throughput Improvement

## Slide 51: DPU Application Runtime
The latency penalty is unacceptable!
2x

## Slide 52: Effectiveness of Data Migration Pipelining (DMP)
We apply DMP technique to each MemBo group to evaluate its effectiveness
Conclusion: the effectiveness of DMP is workload dependent: highly related to the proportion of input data copy time and the reclamation time
DMP significantly reduces the runtime for some workloads

## Slide 53: Evaluation Scenarios
One YCSB workload
  Throughput Improvement of YCSB
  Major page faults reduction
One YCSB workload + one DPU application
  DPU application runtime
  Throughput Improvement of YCSB
  Effectiveness of data migration pipelining
One YCSB workload + multiple DPU applications
  Effectiveness of prediction-based rank reservation (PBRR)
  Throughput Improvement of YCSB

## Slide 54: Scenario 3-One YCSB workload + multiple DPU applications
Evaluation steps
  Launch YCSB A (100M items and operations)
  After 5 minutes, launch a R-rank VA every 1 minute. Each application occupies its DPU ranks for D minutes
  Collect the overall throughput of YCSB A and the reclamation time of each DPU application
Configuration | (R, D)
A | (1, 16)
B | (2, 8)
C | (4, 4)

## Slide 55: Result-Configuration A

## Slide 56: Result-Configuration B

## Slide 57: Result-Configuration C

## Slide 58: Conclusion
We propose MemBo, a runtime memory borrowing mechanism that provides a solution to address memory demand variance on UPMEM servers
Enabling Runtime memory borrowing, increasing the utilization and flexibility of MRAM
MemBo achieves up to 3.43x of throughput improvement and 99.9% of page fault reduction on YCSB workloads

## Slide 59: Thank You